***************Draft***************
Comparing SpinalHDL to Autofpga
When a PLL is required
Lesson Learned
03/22/21
***************Draft***************

The catzip project was created for the CatBoard using software packages (Autofpga, Icestorm, Yosys, Nextpnr, Verilator and ZipCPU).
The main clock on the Catboard is 100MHz. As the logic in FPGA is increased the speed needs to be reduced to obtain a working system. In the catzip.bin require a PLL to reduce the input freqency to 40Mhz.

The first steps in creating the catzip.bin was using Autofpga to generate a toplevel.v and main.v in the folder ~/testbuilds/catzip/rtl/catzip.

Autofpga requires a file ~/testbuilds/catzip/auto-data/clockpll40.txt with the following. Autofpga uses the tags
@$CLKFREQHZ=40000000
@PREFIX=clk
@CLOCK.NAME=clk
@TOP.DEFNS=
wire	s_clk, s_reset;
@TOP.INSERT=
assign	s_reset = 1'b0; // This design requires local, not global resets
@TOP.PORTLIST=i_clk
@TOP.IODECL= input i_clk;
@REGDEFS.H.DEFNS=
#define	CLKFREQHZ	@$CLKFREQHZ
@BDEF.DEFN=
#define	CLKFREQHZ	@$CLKFREQHZ
@CLOCK.NAME=clk
@CLOCK.FREQUENCY= @$CLKFREQHZ

##
##
@$CLKFREQHZ=40000000
@PREFIX=clk
@CLOCK.NAME=clk
@TOP.DEFNS=
wire	s_clk, s_reset;
@TOP.INSERT=
assign	s_reset = 1'b0; // This design requires local, not global resets

`ifdef	VERILATOR
assign	s_clk = i_clk;
`else
wire	clk_40mhz, pll_locked;
SB_PLL40_CORE #(
.FEEDBACK_PATH("SIMPLE"),
.DELAY_ADJUSTMENT_MODE_FEEDBACK("FIXED"),
.DELAY_ADJUSTMENT_MODE_RELATIVE("FIXED"),
.PLLOUT_SELECT("GENCLK"),
.FDA_FEEDBACK(4'b1111),
.FDA_RELATIVE(4'b1111),
.DIVR(4'b0100),	// DIVR = 4
.DIVQ(7'b0011111),	// DIVQ = 31
.DIVF(3'b100),	// DIVF = 4
.FILTER_RANGE(3'b010)	// FILTER_RANGE = 2
) plli (
.REFERENCECLK (i_clk ),
.PLLOUTCORE (clk_40mhz ),
.LOCK (pll_locked ),
.BYPASS (1'b0 ),
.RESETB (1'b1 )
);
       //SB_GB global_buffer(clk_40mhz, s_clk);
assign	s_clk = clk_40mhz;
`endif
@TOP.PORTLIST=i_clk
@TOP.IODECL= input i_clk;
@REGDEFS.H.DEFNS=
#define	CLKFREQHZ	@$CLKFREQHZ
@BDEF.DEFN=
#define	CLKFREQHZ	@$CLKFREQHZ
@CLOCK.NAME=clk
@CLOCK.FREQUENCY= @$CLKFREQHZ

The file /home/devel/testbuilds/catzip/auto-data/Makefile requires the following:

DATA := global.txt bkram.txt buserr.txt clockpll40.txt \
        pic.txt pwrcount.txt version.txt \
        hbconsole.txt gpio.txt dlyarbiter.txt zipbones.txt sdramdev.txt \
        mem_sdram_bkram.txt sdramscope.txt

/home/devel/icestorm/icefuzz/tests/sb_pll40_core.v

module top(
input REFERENCECLK,
output PLLOUTCORE,
output PLLOUTGLOBAL,
input EXTFEEDBACK,
input [7:0] DYNAMICDELAY,
output LOCK,
input BYPASS,
input RESETB,
input LATCHINPUTVALUE,

//Test Pins
output SDO,
input SDI,
input SCLK
);
SB_PLL40_CORE #(
.FEEDBACK_PATH("DELAY"),
// .FEEDBACK_PATH("SIMPLE"),
// .FEEDBACK_PATH("PHASE_AND_DELAY"),
// .FEEDBACK_PATH("EXTERNAL"),

.DELAY_ADJUSTMENT_MODE_FEEDBACK("FIXED"),
// .DELAY_ADJUSTMENT_MODE_FEEDBACK("DYNAMIC"),

.DELAY_ADJUSTMENT_MODE_RELATIVE("FIXED"),
// .DELAY_ADJUSTMENT_MODE_RELATIVE("DYNAMIC"),

.PLLOUT_SELECT("GENCLK"),
// .PLLOUT_SELECT("GENCLK_HALF"),
// .PLLOUT_SELECT("SHIFTREG_90deg"),
// .PLLOUT_SELECT("SHIFTREG_0deg"),

.SHIFTREG_DIV_MODE(1'b0),
.FDA_FEEDBACK(4'b1111),
.FDA_RELATIVE(4'b1111),
.DIVR(4'b0000),
.DIVF(7'b0000000),
.DIVQ(3'b001),
.FILTER_RANGE(3'b000),
.ENABLE_ICEGATE(1'b0),
.TEST_MODE(1'b0)
) uut (
.REFERENCECLK (REFERENCECLK ),
.PLLOUTCORE (PLLOUTCORE ),
.PLLOUTGLOBAL (PLLOUTGLOBAL ),
.EXTFEEDBACK (EXTFEEDBACK ),
.DYNAMICDELAY (DYNAMICDELAY ),
.LOCK (LOCK ),
.BYPASS (BYPASS ),
.RESETB (RESETB ),
.LATCHINPUTVALUE(LATCHINPUTVALUE),
.SDO (SDO ),
.SDI (SDI ),
.SCLK (SCLK )
);
endmodule

Using SpinalHDL to create pll Verilog.

The file /home/devel/SpinalKeyboardtest/src/main/scala/testcode/toplevel.scala is what determines the what is placed in the file /home/devel/SpinalKeyboardtest/toplevel_pll.v The first is used to separate the code into a package. The green highlted area are just comments.

package testcode

import spinal.core._
/*
`ifdef	VERILATOR
assign	s_clk = i_clk;
`else
wire	clk_40mhz, pll_locked;
SB_PLL40_CORE #(
.FEEDBACK_PATH("SIMPLE"),
.DELAY_ADJUSTMENT_MODE_FEEDBACK("FIXED"),
.DELAY_ADJUSTMENT_MODE_RELATIVE("FIXED"),
.PLLOUT_SELECT("GENCLK"),
.FDA_FEEDBACK(4'b1111),
.FDA_RELATIVE(4'b1111),
.DIVR(4'b0100),	// DIVR = 4
.DIVQ(7'b0011111),	// DIVQ = 31
.DIVF(3'b100),	// DIVF = 4
.FILTER_RANGE(3'b010)	// FILTER_RANGE = 2
) plli (
.REFERENCECLK (i_clk ),
.PLLOUTCORE (clk_40mhz ),
.LOCK (pll_locked ),
.BYPASS (1'b0 ),
.RESETB (1'b1 )
);
       //SB_GB global_buffer(clk_40mhz, s_clk);
assign	s_clk = clk_40mhz;
`endif

  SB_PLL40_CORE #(
    .FEEDBACK_PATH("SIMPLE"),
    .DIVR(4'b0010),
    .DIVF(7'h16),
    .DIVQ(3'b110),
    .FILTER_RANGE(3'b010)
  ) plli (
    .REFERENCECLK (io_CLK_100 ), //i
    .PLLOUTCORE (plli_PLLOUTCORE ), //o
    .LOCK (plli_LOCK ), //o
    .BYPASS (_zz_1 ), //i
    .RESETB (_zz_2 ) //i
  );
  assign _zz_1 = 1'b0;
  assign _zz_2 = 1'b1;
*/

package testcode

import spinal.core._
case class SB_PLL40_CORE() extends BlackBox {
  val REFERENCECLK: Bool = in Bool
  val PLLOUTCORE, LOCK = out Bool
  val BYPASS = in Bits()
  val RESETB = in Bits()
  addGeneric("FEEDBACK_PATH", "SIMPLE")
  addGeneric("DELAY_ADJUSTMENT_MODE_FEEDBACK", "FIXED")
  addGeneric("DELAY_ADJUSTMENT_MODE_RELATIVE", "FIXED")
  addGeneric("PLLOUT_SELECT","GENCLK")
  addGeneric("FDA_FEEDBACK",B(15,4 bits))
  addGeneric("FDA_RELATIVE",B(15,4 bits))
  addGeneric("DIVR", B(0,4 bits))
  addGeneric("DIVQ", B(4,3 bits))
  addGeneric("DIVF", B(7,7 bits))

  addGeneric("FILTER_RANGE", B(5,3 bits))

  //addGeneric("BYPASS", B(0,1 bits))
  //addGeneric("RESETB", "RESET")
  //addGeneric("EXTFEEDBACK","()")
}
case class main() extends BlackBox {
val iClk: Bool = in Bool
val iRX: Bool = in Bool
val oTX: Bool = out Bool

}
class toplevel_pll() extends Component {
  val io = new Bundle() {
  val CLK_100 = in Bool
  val uartRX = in Bool
  val uartTX = out Bool

  }
  val plli: SB_PLL40_CORE = new SB_PLL40_CORE()
  plli.REFERENCECLK <> io.CLK_100
  plli.BYPASS <> B(0,1 bit)
  plli.RESETB <> B(1,1 bit)

  val main = new main()
  main.iClk <> plli.PLLOUTCORE
  main.iRX <> io.uartRX
  main.oTX <> io.uartTX
}
//Generate the toplevel_pll Verilog
object toplevel_pllVerilog {
  def main(args: Array[String]) {
    SpinalVerilog(new toplevel_pll)
  }
}

Goal: To complete the SIMPLE pll using SpinalHDL. In addition to include a Blackbox to include main.v
a MyHDL modude which sends HELLOWORLD at 2MBaud. The PLL will reduce the 100MHz and main was reduced to
115200 Baud.

Status as of 03/22/21: The SIMPLE pll appears to be complete, but the HELLOWORLD at 115200 Baud is now
working. main.pcf -> toplevel_pll.pcf. Yosys, Nextpnr, icetime, and icepack are all working.
main require a active lo iRst which was provided by pwruprst.py

  wire [0:0] _zz_1;
  wire [0:0] _zz_2;
  wire plli_PLLOUTCORE;
  wire plli_LOCK;
  wire main_1_oTX;

  SB_PLL40_CORE #(
    .FEEDBACK_PATH("SIMPLE"),
    .DELAY_ADJUSTMENT_MODE_FEEDBACK("FIXED"),
    .DELAY_ADJUSTMENT_MODE_RELATIVE("FIXED"),
    .PLLOUT_SELECT("GENCLK"),
    .FDA_FEEDBACK(4'b1111),
    .FDA_RELATIVE(4'b1111),
    .DIVR(4'b0000),
    .DIVQ(3'b100),
    .DIVF(7'h07),
    .FILTER_RANGE(3'b101)
  ) plli (
    .REFERENCECLK (io_CLK_100 ), //i
    .PLLOUTCORE (plli_PLLOUTCORE ), //o
    .LOCK (plli_LOCK ), //o
    .BYPASS (_zz_1 ), //i
    .RESETB (_zz_2 ) //i
  );
  main main_1 (
    .iClk (plli_PLLOUTCORE ), //i
    .iRX (io_uartRX ), //i
    .oTX (main_1_oTX ) //o
  );
  assign _zz_1 = 1'b0;
  assign _zz_2 = 1'b1;
  assign io_uartTX = main_1_oTX;

Testing 100MHz and BAUDRATE 2e6

mainwkg1.png

mainwkg2.png

devel@mypi3-21:~/myhdl-relook/rs232tests $ sudo config_cat main.bin

mainwkg3.png

~/SpinalKeyboardtest/rs232-MyHDL-SpinalHDL

diff rs232sig.py ~/myhdl-relook/rs232tests/rs232sig.py
3,4c3,4
< Clk_f=50e6 #100 Mhz
< BAUDRATE=115200
---
> Clk_f=100e6 #100 Mhz
> BAUDRATE=2e6

In main.py uncoment
133 #convert_main(hdl='Verilog')

python main.py create main.v

~/SpinalKeyboardtest/
sbt "runMain testcode.toplevel_pllVerilog"

[info] welcome to sbt 1.3.13 (Raspbian Java 11.0.9.1)
[info] loading settings for project spinalkeyboardtest-build from plugins.sbt ...
[info] loading project definition from /home/devel/SpinalKeyboardtest/project
[info] loading settings for project spinalkeyboardtest from build.sbt ...
[info] set current project to SpinalTemplateSbt (in build file:/home/devel/SpinalKeyboardtest/)
[warn] Multiple main classes detected. Run 'show discoveredMainClasses' to see the list
[info] running (fork) testcode.toplevel_pllVerilog
[info] [Runtime] SpinalHDL v1.4.3 git head : adf552d8f500e7419fff395b7049228e4bc5de26
[info] [Runtime] JVM max memory : 944.0MiB
[info] [Runtime] Current date : 2021.03.22 06:27:57
[info] [Progress] at 0.000 : Elaborate components
[info] [Progress] at 0.361 : Checks and transforms
[info] [Progress] at 0.605 : Generate Verilog
[info] [Warning] 1 signals were pruned. You can call printPruned on the backend report to get more informations.
[info] [Done] at 0.912
[success] Total time: 7 s, completed Mar 22, 2021, 6:27:59 AM

~/SpinalKeyboardtest/rs232-MyHDL-SpinalHDL
rm -f toplevel_pll.v

cat ../toplevel_pll.v main.v > toplevel_pll.v

yosys -l simple.log -p 'synth_ice40 -abc9 -blif toplevel_pll.blif -json toplevel_pll.json' toplevel_pll.v
=== toplevel_pll ===

   Number of wires: 319
   Number of wire bits: 526
   Number of public wires: 319
   Number of public wire bits: 526
   Number of memories: 0
   Number of memory bits: 0
   Number of processes: 0
   Number of cells: 501
     SB_CARRY 116
     SB_DFFE 73
     SB_DFFER 46
     SB_DFFESR 4
     SB_DFFR 4
     SB_DFFS 1
     SB_DFFSR 32
     SB_DFFSS 2
     SB_LUT4 222
     SB_PLL40_CORE 1

nextpnr-ice40 --hx8k --pcf toplevel_pll.pcf --json toplevel_pll.json --asc toplevel_pll.asc

icetime -d hx8k -c 50 toplevel_pll.asc
// Reading input .asc file..
// Reading 8k chipdb file..
// Creating timing netlist..
// Timing estimate: 9.39 ns (106.46 MHz)
// Checking 20.00 ns (50.00 MHz) clock constraint: PASSED.

icepack toplevel_pll.asc toplevel_pll.bin

md5sum toplevel_pll.bin

endmodule